## Slide 1: Adders Mania
Cairo University Faculty of Engineering Computer Engineering Department CMP3020

## Slide 2: Team
Name | Sec | B.N. | Code
Abdelrahman Mohamed Abdelfattah | 1 | 22 | 9210587
Osama Saleh Farag | 1 | 12 | 9210195
Amr Salahuddin Fouad | 1 | 29 | 9210774
Abdelrahman Mohamed Hefney | 1 | 21 | 9210584

## Slide 3: Verilog Adder
Code

## Slide 4: Ripple Carry Adder
It uses Smaller Module Traditional Full adder (FA)
It’s Code:

## Slide 5: Ripple Carry Adder
Ripple Carry Code:

## Slide 6: Carry Select Adder
It uses 3 Ripple Carry adders of 16-bits, The first 16-bits carry output selects the correct output from the second 16 Ripple carry Adder.
Carry Select Code:
Instantiation of Modules

## Slide 7: Carry Select Adder
Output Selection:

## Slide 8: Carry Bypass
It Enhances Ripple carry Adder, as it sees if the carry propagate is 1 in every bit, the carry out will be the carry in.
We divided the 32-bits adder into 8 4-bit adders, each block has the architecture found in this schematic

## Slide 9: Carry Bypass
4-bit Carry Bypass Code:

## Slide 10: Carry Bypass
Carry Bypass 32-bit Code:

## Slide 11: Carry Lookahead
Code:
Notes: module CarryLookAheadAdder2(
input wire [31:0]a,
input wire [31:0]b,
input wire Cin,
output wire [31:0]S,
output wire Cout,
output wire Overflow
);
wire [32:0] G;
wire [31:0] P;
assign P[31:0] = a ^ b;
assign G[32:1] = a & b;
assign G[0] = Cin;
wire [32:0] Carry;
assign Carry[0] = Cin;
genvar i , j , k;
generate
for (i = 1;i < 33;i = i + 1) begin : gen_block1
wire [i:0] Ps;
assign Ps[0] = 1'b1;
for (k = 0;k < i;k = k + 1) begin : gen_block2
assign Ps[k + 1] = Ps[k] & P[i - k - 1];
end
wire [i:0] terms;
assign terms[0] = G[i];
for (k = 0;k < i;k = k + 1) begin : gen_block3
assign terms[k + 1] = terms[k] | (Ps[k + 1] & G[i - k - 1]);
end
assign Carry[i] = terms[i];
assign S[i - 1] = Carry[i - 1] ^ P[i - 1];
end
endgenerate
assign Cout = Carry[32];
assign Overflow = (a[31] == b[31]) & (a[31] != S[31]);
endmodule

## Slide 12: Test Bench
Code:

## Slide 13: Results
Verilog Adder

## Slide 14: Results
Ripple Carry Adder
Changes in Test Bench

## Slide 15: Results
Ripple Carry Adder

## Slide 16: Results
Carry Select Adder
Changes in Test Bench

## Slide 17: Results
Carry Select Adder

## Slide 18: Results
Carry Bypass
Changes in Testbench

## Slide 19: Results
Carry Bypass

## Slide 20: Results
Carry Look ahead
Changes in Test Bench

## Slide 21: Results
Carry Look ahead

## Slide 22: Synthesis Results
Adder Type Properties | Verilog ‘+’ | Carry Bypass | Carry Select | Carry Lookahead | Ripple Carry
Max Delay | 12.26 ps | 11.57 ps | 8.24 ps | 4.6 ps | 14.19 ps
Min Delay | 1.69 ps | 1.63 ps | 1.67 ps | 1.68 ps | 1.67 ps
Total Power | 403.8777 uW | 518.7082 uW | 980.5375 uW | 790.9255 uW | 629.3212 uW
Area | 976.895985 | 1360.281605 | 2123.366425 | 2611.814410 | 1301.299213
Number of Combinational Cells | 35 | 99 | 164 | 280 | 99

## Slide 23: Floating Point Adder
We chose The Time Design Metric to implement this adder, so we chose Carry Lookahead adder.
Code:

## Slide 24: Floating Point
Continue Code:

## Slide 25: Floating Point
Continue Code

## Slide 26: Floating Point

## Slide 27: Floating Point
End

## Slide 28: Floating Point Simulation Result

## Slide 29: Floating Point Synthesis Result
Adder Type Properties | Floating Point Adder
Max Delay | 13.59 ps
Min Delay | 6.38 ps
Total Power | 2.8615e+03 uW
Area | 12624.421156
Number Combinational Cells | 1163